## Slide 1: WattWatch
HACKATHON PITCH · CAMPUS ENERGY
See where campus electricity goes, and stop paying to light and cool empty rooms.
ESP32 room sensors
Live campus map
Telegram alerts
Relay shutoff
The live dashboard: every room's status, cost per hour and the campus map
Notes: Open with the hook: every empty classroom with the lights, fans and AC running is money the campus pays for nothing. WattWatch makes that waste visible room by room and switches it off.

## Slide 2: Our campus pays to light and cool empty rooms
15%
of the electricity bill is avoidable, mostly rooms running with no one inside
70 min
is how long a room typically stays powered after the last class ends
0
rooms where anyone can see live usage today. The bill arrives once a month
Room 204, Block B, 1:44 PM. Two ACs and ten lights have been running for 2 h 04 m since the 10:40 lecture ended. Nobody knows, so nobody switches them off. That one room loses about ₹35 every hour.
Figures from our pilot simulation of 20 rooms and six building feeders, at ₹9 per kWh.
Notes: Three numbers carry the problem: the waste is real, it happens after class, and nobody can see it. Then make it concrete with Room 204.

## Slide 3: A ₹800 sensor in every room, one live view of the campus
Sense
ESP32 with an SCT-013 current clamp and a PIR presence sensor
Send
Readings every 2 seconds over MQTT to HiveMQ Cloud
Store
FastAPI backend with InfluxDB for the time series
Learn
Prophet forecasts tomorrow; Isolation Forest flags odd spikes
Act
Dashboard, Telegram alert to the in-charge, relay cuts power
Presence only, no cameras. The PIR sensor reports whether a room is occupied, never who is in it. If the timetable says no class and the sensor sees no one, the room should be off.
Notes: Walk left to right: sense, send, store, learn, act. Stress that it is cheap off-the-shelf hardware and that privacy is built in: no cameras.

## Slide 4: Every room, live, in one place
Room page: live power, today's cost by hour and the turn-off button
Live campus map
Buildings and rooms coloured by load, with cost per hour on every pin.
Waste alerts
Empty with power on for 15 minutes sends a Telegram message to the building in-charge.
One-tap shutoff
The relay cuts the AC and light circuits. Motion turns them back on.
Notes: Show the room page. Then switch to the live site: open Room 204, press Turn off power, and watch the status, the drawing and the cost update.

## Slide 5: It learns the campus and predicts tomorrow
Chart: Campus load, kW
| 12a | 1a | 2a | 3a | 4a | 5a | 6a | 7a | 8a | 9a | 10a | 11a | 12p | 1p | 2p | 3p | 4p | 5p | 6p | 7p | 8p | 9p | 10p | 11p
Tomorrow (forecast) | 168 | 106 | 106 | 106 | 106 | 106 | 191 | 191 | 459 | 587 | 614 | 617 | 595 | 501 | 593 | 578 | 561 | 425 | 291 | 308 | 259 | 259 | 247 | 226
Today | 158 | 103 | 104 | 100 | 97 | 96 | 178 | 185 | 450 | 562 | 565 | 557 | 548 | 480 | 582 | 559 | 522 | 385 | 266 | 292 | 253 | 252 | 233 | 206
617 kW
expected peak tomorrow at 11 AM. Pre-cooling Block B before 10 AM trims about ₹1,200 off it.
7 kW
drawn by Computer Lab 3 from midnight to 7 AM on Sunday. Flagged automatically: PCs and lights left on.
Notes: Forecasting uses past load, the timetable and the weather. Anomaly detection compares each room and building with its own usual for that hour.

## Slide 6: Pays for itself in under three months
₹1.59 L
saved every month
12.7 t
CO₂ avoided each month
2.3 months
hardware payback
₹800
hardware per room
Chart: Where the saving comes from (₹ per month)
| Switch off ACs 10 min after class | Auto shutoff after 20 min empty | AC set to 24°C instead of 22°C
Monthly saving | 76376 | 45378 | 37622
Scales to any campus
420 rooms × ₹800 plus one gateway per 40 rooms comes to ₹3.6 lakh in hardware.
Start with the worst block, prove the saving in 30 days, then grow.
Notes: Lead with rupees and CO2, not kWh. All numbers come from the planner on the website, so judges can change the sliders and see the result live.

## Slide 7: See it live
1
Leave the room empty
Bulb and fan on, nobody inside. The sensor sees no motion.
2
Alert lands on the phone
Telegram message to the in-charge with the ₹ lost so far.
3
Relay cuts the power
The dashboard shows the room off and the rupees being saved.
What we need next
One academic block for a 30-day pilot
Last year's electricity bills from the admin office
Help from an electrician to fit the relays
Thank you. Questions?
Notes: Run the live demo with the real ESP32 node: leave the room empty, show the Telegram alert, and let the relay cut power. Then ask for the pilot.